## Slide 1: Environmental Modeling Basic GIS Modeling Suitability Index Modeling

## Slide 2: GIS Modeling Approaches
GIS by itself
GIS integrated with statistics
GIS integrated with process models

## Slide 3
1. The Delphi Approach
A procedure for obtaining and processing expert judgments to maximize the accuracy of the resulting estimates
Main considerations - Data, budget, and time can be constrained for a scientific evaluation - Human mind is capable of making quite accurate judgments

## Slide 4
1. Delphi
Experts' role
1. select appropriate variables
2. estimate the magnitude of ranking
3. assign weights to variables

## Slide 5
1. Delphi
The Delphi steps
1. ask each expert for an independent opinion on carefully prepared questions
2. calculate the median and range of opinions and feed these back to the experts for another round of estimate
3. repeat step 1 and 2 for a few rounds
4. use the median of the final round as the best answer
* time and cost factors

## Slide 6: Simple Modeling
Ranking and weighting
M Ruvane, UNC Chapel Hill

## Slide 7
2. Land Suitability Analysis
Richmond Parkway, NY evaluation
McHarg, I.L., 1969. Design with Nature
Korean War Veterans Parkway, in Staten Island http://en.wikipedia.org/wiki/Richmond_Parkway_%28Staten_Island%29

## Slide 8
2. Land Suitability Analysis
A total of 16 land variables e.g. slope, drainage, land values, etc.
Each variable is ranked from 1 to 3 e.g. slope<2.5%,3; 2.5%<slope<10%,2; slope>10%,1
The grand index
= summation of ranking * weighting

## Slide 9: Ian McHarg Richmond Parkway
Slope
zone 1: slope > 10%
zone 2: 2.5% < slope < 10%
zone 3: slope < 2.5%
Surface drainage
zone 1: streams, lakes, and ponds
zone 2: natural drainage channels
zone 3: absence of surface water

## Slide 10: Ian McHarg Richmond Parkway
Soil drainage
Bedrock foundation
Soil foundation
Susceptibility to erosion
Land values
Tidal inundation

## Slide 11: Ian McHarg Richmond Parkway
Historic values
Scenic values
Recreation values
Water values
Forest values
Wildlife values
Residential values
Institutional values

## Slide 13: Ranking and Weighting
1.0
0.8
0.6
0.4
0.2
1.0
0.8
0.6
0.4
0.2
20 40 60 80 100%
20 40 60 80 100%
20 40 60 80 100%
1.0
0.8
0.6
0.4
0.2
1.0
0.8
0.6
0.4
0.2
20 40 60 80 100%
Carrying capacity for grazers
Man-made water loss/total
Dissolved Oxygen
Density of man-made structures

## Slide 14
3. The DRASTIC Model
Development
- By the National Water Well Association in 1987 for US EPA to evaluate groundwater pollution potential.
- It used the Delphi method to design parameters by compiling responses from more than 40 of the nation's leading groundwater scientists.

## Slide 15
3. DRASTIC
The model D - Depth to water table R - Recharge A - Aquifer media S - Soil media T - Topography I - Impact of vadoes zone C - Conductivity of the aquifer

## Slide 16
Range Rating
0-5 10
5-15 9
15-30 7
30-50 5
50-75 3
75-100 2
100+ 1
Ranges and Ratings
for Depth to Water
Depth to Water (Feet)
Ranges and Ratings
for Net Recharge
Net Recharge (inches)
Range Rating
0-2 1
2-4 3
4-7 6
7-10 8
10+ 9

## Slide 17
Ranges and Ratings
for Aquifer Media
Aquifer Media
Ranges Rating
Massive Shale 2
Metamorphic/Igneous 3
Weathered Metamorphic/
Igneous 4
Glacial Till 5
Bedded Sandstone, Limestone
And Shale Sequences 6
Massive Sandstone 6
Massive Limestone 6
Sand and Gravel 8
Basalt 9
Karst Limestone 10
Ranges and Ratings
for Soil Media
Soil Media
Ranges Rating
Thin or Absent 10
Gravel 10
Sand 9
Peat 8
Shrinking and/or
Aggregated Clay 7
Sandy Loam 6
Loam 5
Silty Loam 4
Clay Loam 3
Muck 2
Nonshrinking and
Nonaggregated Clay 1

## Slide 18
Ranges and Ratings
for Topography
Topography (Percent Slope)
Range Rating
0-2 10
2-6 9
6-12 5
12-18 3
18+ 1
Ranges and Ratings
for Impact of the Vadose Zone Impact of the Vadose Zone Media
Range Rating
Confining Layer 1
Silt/Clay 3
Shale 3
Limestone 6
Sandstone 6
Bedded Limestone,
Sandstone, Shale 6
Sand and Gravel with
significant Silt and Clay 6
Metamorphic/Igneous 4
Sand and Gravel 8
Basalt 9
Karst Limestone 10

## Slide 19
Ranges and Ratings
for Hydraulic Conductivity
Hydraulic Conductivity (GPD/FT2)
Range Rating
1-100 1
100-300 2
300-700 4
700-1000 6
1000-2000 8
2000+ 10

## Slide 20
4. The Judgment Impact Matrix
It suits for evaluation of complex systems
Estimation structure components -> environmental elements -> societal elements -> grand index
The matrix components x link (0,1) x element set1 x element set2 x weights (for element 2)
The links, environmental, societal and weights can be determined by the Delphi method

## Slide 21
4. JIM
Element i
Element 2
Element 1
Element m
Policy
Element i
Element 2
Element 1
Element m
Component 1
Component 2
Component i
Component m

## Slide 22: 5. A Mock Project
What is the problem
Where to spray to control mosquito pop
Factors that affect spray
1: areas of high human pop density
2: adjacent to water bodies
3: low elevation
Find data for each factor
Apply functions to the data

## Slide 23: Find Data
Factor 1:
areas of high
population
density
R Brancoto, SUNY Buffalo

## Slide 24: Find Data
Factor 2:
adjacent to
water
Function:
buffer
T Tatignani, SUNY BUffalo

## Slide 25: Function
Function: Buffer width =
Points Lines Polygons
M Ruvane, UNC Chapel Hill
Notes: Buffer: A zone constructed outward from an isolated object (point or line) to a specific distance.
Setback: A zone inside a POLYGON constructed by a fixed distance from the edge of the polygon; typically used to restrict building or activities too close to the edge of a property parcel.

## Slide 26: Find Data
Factor 3:
low elevation
NIMA & NASA

## Slide 27: Ranking and Weighting
Suitability = Layer1*1 + Layer2*3 + layer3*3
M Ruvane, UNC Chapel Hill

## Slide 28
Slope
Aspect
Distance to roads
Distance to trails
From Richard Aspinall

## Slide 29: Suitability Index Modeling
Owen Earley, GIS/EM4 2000