## Slide 1
Environmental Modeling
Weighting GIS Layers

## Slide 2: 1. A Hydrologic Model
To estimate groundwater recharge in order to issue water pump permission
Statistics: Multiple Regression
Sophocleous, M., 1992. Groundwater recharge estimation and regionalization: the Great Bend Prairie of central Kansas and its recharge statistics. Journal of Hydrology, 137:113-140.

## Slide 3: 2. Variables
Dependent variable:
groundwater recharge

## Slide 4: 2. Variables
Independent variables:
1. annual precipitation
2. soil-profile water storage during spring
3. depth to water table in spring
4. spring precipitation rate = spring precip/# of spring precip days
5. number of precip days during the year

## Slide 5
At each location, collect values for both the dependent variable and the independent variables

## Slide 6: 3. Regression
Independent variables 1-4 are included in the regression
Variable 5 is excluded because
the level of sig> 0.05 for F test
Recharge = -48.8347 + 0.1917X1 - 0.0829X2
- 4.9594X3 + 5.3639X4
R2 = 0.76

## Slide 7: 3. Regression
Recharge = -145.6206 + 0.3449 precip
R2 = 0.5793
Recharge = -48.2453 + 0.2869 precip - 0.1097 soil water
R2 = 0.6895
Recharge = -9.3727 + 0.2459 precip - 0.0819 soils water
– 5.2387 water level
R2 = 0.7381
Recharge = -48.8347 + 0.1917 precip - 0.0829 soil water
– 4.9594 water level +5.3639 precip rate
R2 = 0.7575

## Slide 8: Regression Results
Analysis of variance
DF Sum of Squares Mean Square
Regression 3 97747.09184 32583.03061
Residual 36 7061.68316 196.15787
F = 166.10616 Signif F = 0.0000
Multiple r 0.87328
R Square 0.76262
Adjusted R Square 0.75701
Standard Error 14.00564

## Slide 9: Regression Results
Variables in the Equation
Variable b Se b Beta t Sig t
X1 0.1917 0.001715 0.725998 6.262 0.0000
X2 -0.0829 0.001219 -0.994050 -16.161 0.0000
X3 -4.9594 11.079785 -0.052423 -0.4841 0.0310
X4 5.3639 7.3908 7.9273 -0.932 0.0926
Recharge =
-48.8347 + 0.1917prcip - 0.0829soil water - 4.9594water level + 5.3639precip rate

## Slide 10: 4. GIS Overlay
Extend the site-specific relationship to the entire study area
The regression establishes a quantitative relationship between recharge and the independent variables
Recharge = -48.8347 + 0.1917X1 - 0.0829X2
- 4.9594X3 + 5.3639X4
Recharge(s) = -48.8347 + 0.725998X1
- 0.994050X2 - 0.052423X3 + 7.9273X4

## Slide 11: 4. GIS Overlay
This result is derived from point locations. We need to estimate recharge for the entire study area

## Slide 13: 4. GIS Overlay
For any location that has values for the four independent variables, we can calculate the recharge for that location
The values of the four independent variables can be obtained from GIS layers, one layer for each independent variable

## Slide 14: 4. GIS Overlay
GIS layers
1. annual precipitation, NCDC, spatial
interpolation
2. spring soil storage, data?
3. depth to water table, well log, spatial
interpolation
4. spring precipitation rate, climatic
stations

## Slide 15
X1: Annual Precipitation

## Slide 16
X2: Spring Soil Storage

## Slide 17
X3: Depth to Water Table

## Slide 18
X4: Spring precipitation Rate

## Slide 19: 4. GIS Overlay
Recharge potential =
- 48.8347
+ 0.1917 X1 (annual precip)
- 0.0829 X2 (spring soil storage)
- 4.9594 X3 (depth to water table)
+ 5.3639 X4 (spring precip rate)
The result is a potential groundwater recharge map with a 0.76 accuracy

## Slide 21
Independent Variable 1: Land Cover Change

## Slide 22
Independent Variable 2: Human Development Index

## Slide 23
Independent Variable 3: Population Value

## Slide 24
Independent Variable 4: Land Cover

## Slide 25
Independent Variable 5: Soil Moisture

## Slide 26
Dependent Variable: Predicted Land Cover

## Slide 27
Results