## Slide 1
Spatial Interpretation

## Slide 2: 1. Definition
A procedure of estimating the values of properties at un-sampled sites
The property may be interval/ratio values, can be nominal and ordinal
The rational behind is that points close together in space are more likely to have similar values than points far apart

## Slide 4: 2. Terminology
Point vs. line vs. areal interpolation point - point, point - line, point - areal

## Slide 5: 2. Terminology …
Global vs. local interpolation
  Global - apply a single function across the entire region
  Local - apply an algorithm to a small portion at a time

## Slide 6: 2. Terminology …
Exact vs. approximate interpolation
  exact - honor the original points
  approximate - when uncertainty is involved in the data
Gradual vs. abrupt

## Slide 7: 3. Interpolation - Linear
Linear interpolation
Known values
Known and predicted values after interpolation

## Slide 8: 3. Interpolation - Linear
Assume that changes between two locations are linear

## Slide 9: 3. Interpolation - Proximal
Thiesson polygon approach
Local, exact, abrupt
Perpendicular bisector of a line connecting two points
Best for nominal data

## Slide 10: Construction of Polygon
+ 130
+ 150
+ 200
+ 180
+ 130
Polygon of influence for x=180

## Slide 11: Construction of Polygon..
+ 130
+ 150
+ 200
+ 180
+ 130
Draw line segments between x and other points

## Slide 12: Construction of Polygon..
+ 130
+ 150
+ 200
+ 180
+ 130
Find the midpoint and bisect the lines.

## Slide 13: Construction of Polygon..
+ 130
+ 150
+ 200
+ 180
+ 130
Extend the bisecting lines till adjacent ones meet.

## Slide 14: Construction of Polygon..
+ 130
+ 150
+ 200
+ 180
+ 130
Continue this process.

## Slide 15: 3. Interpolation - Proximal

## Slide 16: 3. Interpolation – Proximal ..
http://gizmodo.com/5884464/

## Slide 18: 3. Interpolation – B-spline
Local, exact, gradual
Pieces a series of smooth patches into a smooth surface that has continuous first and second derivatives
Best for very smooth surfaces e.g. French curves

## Slide 19: 3. Interpolation – Trend Surface
Trend surface - polynomial approach
Global, approximate, gradual
Linear (1st order): z = a0 + a1x + a2y
Quadratic (2nd order):
z = a0 + a1x + a2y + a3x2
+ a4xy + a5y2
Cubic etc.
Least square method

## Slide 20
Trends of one, two, and three independent variables for polynomial equations of the first, second, and third orders (after Harbaugh, 1964).

## Slide 21: 3. Interpolation – Inverse Distance
Local, approximate, gradual S wizi 1 z = --------, wi = -----, or wi = e -pdi etc. S wi dip

## Slide 22: 3. Interp – Fourier Series
Sine and cosine approach
Global, approximate, gradual
Overlay of a series of sine and cosine curves
Best for data showing periodicity

## Slide 23: 3. Interp – Fourier Series

## Slide 24: 3. Interp – Fourier Series
Fourier series
Single harmonic in X1 direction
Two harmonics in X1 direction
Single harmonic in both X1 and X2 directions
Two harmonics in both directions

## Slide 26: 3. Interp - Kriging
Kriging - semivariogram approach, D.G. Krige
Local, exact, gradual
Spatial dependence (spatial autocorrelation)
Regionalized variable theory,
by Georges Matheron
A situation between truly random and deterministic
Stationary vs. non-stationary

## Slide 27: 3. Kriging
First rule of geography:
Everything is related to everything else. Closer things are more related than distant things
By Waldo Tobler

## Slide 29: 3. Interp - Kriging
Semivariogram 1 n g(h) = ------ S (Zi - Zi+h)2 2n i=1
Sill, range, nugget
Sill
Range
Lag distance (h)
Semivariance

## Slide 30: 3. Kriging
Isotropy vs. anisotropy

## Slide 31: 4. Summary Statistics
Parameters (for populations) m, s2, s
Statistics (for samples), x, S2, S

## Slide 32: 4. Basic Statistics
Measures of location
mean, median, mode, minimum,
maximum, lower and upper quartiles
Measures of spread
variance, standard deviation
Correlation
covariance, correlation coefficient